GPS Tracker User Manual

Preface

Thank you for purchasing the tracker. This manual shows how to operate the device smoothly and correctly. Make sure to read this manual carefully before using this product. Please note that specification and information are subject to changes without prior notice in this manual.

Any change will be integrated in the latest release. The manufacturer assumes no responsibility for any errors or omissions in this document.

# ◆Quick using

1）Open device case, proper insert GSM card, connect external power supply, Must turn on small switch inside SIM card hole.

2） Put device outside, around 30s three lights will keep lighting on stands

for device can work normally.

## Specifications

| Content | Specs. |
| --- | --- |
| Dim. | 80mm x 33mm x 22mm |
| Weight | 50g |
| Network | 4G+2G network |
| Band | LTE-FDDB1/B2/B3/B4/B5/B7/B8/B28/B66 GSM 850/900/1800/1900MHz GSM 850/900/1800/1900MHz |
| GPS chip | SIMCOM |
| GSM module | SIMCOM7670SA |
| GPS sensitivity | -159dBm |
| GPS accuracy | 5m |
| Time To First Fix | Cold status 45s Warm status 35s Hot status 1s |
| Work voltage | 9V-80V |
| Storage Temp. | -40°C to +85°C |
| Operation Temp. | -20°C to +55°C |

# ◆Installation attentions

### NOTE: device front side towards the sky.

When install in car, if the windscreen glued by metal thermal insulation layer or heating layer, it will reduce the GPS receive signal and lead to GPS work disorder.

Device light description

| Light | Represents |
| --- | --- |
| yellow | GSM signal normal |
| blue | GPS signal normal |
| Red | Power |

## 1.Installation instructions

### Preparation

      - Open the package to check the device model number is correct, be with full accessories, or else please contact your supplier;

Choose SIM card, need insert a GSM SIM card into the device, please refer to the suggestion of your supplier for SIM card choice.

Notice:

### Please insert SIM card before turning the device power switch to on;

The SIM card need open the GPRS function;

Please make sure SIM card with full balance.

## Device wiring requirements

3. SMS command list

| Number | Functional item | SMS command | Command reply |
| --- | --- | --- | --- |
| 1 | Restore the initial settings except IP, port, APN | FORMAT | FORMAT |
| 2 | APN query | APN# | Reply：APN:cmnet,, |
| 3 | APN set | APN,cmnet,,# APN,cmnet,aaa,bbb# | Command expmaple: APN,cmnet,,# Cmnet is APN,it has no user name and password Example: APN,cmnet,internet,cmnet# Cmnet is APN,internet is APN user name,cmnet is APN password |
| 4 | Server parameter query | SERVER# | Reply：SERVER:0,103.44.239.119,8011,0 |
| 5 | Server parameter settings | 1、Set the domain name: SERVER, 1, domain name, port, 0# 2、Set IP: SERVER, 0, IP, port, 0 # The last 0 represents: TCP | SMS:SERVER,0,154.23.114.25,8011,0# Reply：SERVER:0,154.23.114.25,8011,0 |
| 6 | Address query (abroad) | URL# | <03-20 22:45>http://maps.google.com/maps?q=+22.601862,+113.832383 |
| 7 | Status query | STATUS# | Battery:4.23V;GPRS:Offline;GSMSignal Level:25;ACC:OFF;GPS:OFF;Defense:ON; |
| 8 | Query parameter settings | PARAM# | IMEI:123456781911111;TIMER:10,3600;SNEDS:3;HBT:180Sec;Defense:2; |
| 9 | Restart command | RESET# | Reply：RESET OK |
| 10 | Query the oil and electricity control status | RELAY# | Reply：RELAY:0 |
| 11 | Oil and electricity control | RELAY,1# RELAY,0# 0 Turn on oil and electricity，1 disconnect oil and electricity | Reply：RELAY 1 OK |
| 12 | Add center number1 | CENTER,A,center number# | SMS：CENTER,A,8618575518750# Reply：CENTER,A:8618575518750 (86 is China country code) |
| 13 | Delete center number1 | CENTER,D# | Reply：CENTER Del OK |
| 14 | Add center number2 | CENTER,A2,center number# | SMS：CENTER,A2,8618007931238# Reply：CENTER,A2:8618007931238 |
| 15 | Delete center number2 | CENTER,D2# | Reply：CENTER D2 Del OK |
| 16 | Add center number3 | CENTER,A3,center number# | SMS：CENTER,A3,8613912345678# Reply：CENTER,A3:8613912345678 |
| 17 | Delete center number3 | CENTER,D2# | Reply：CENTER D3 Del OK |
| 18 | Query center number | CENTER# | Reply：CENTER,A:8618575518750 CENTER,A2:8618007931238 CENTER,A3:8613912345678 |
| 19 | Add SOS number | SOS,A,number 1,number 2,number 3# | SOS,A,8618575518750# SOS,A,8613912345678,8618007931238# SOS,A,8613912345678,8613912345678,8613912345678# Option to set 1 or more numbers at a time |
| 20 | Delete SOS number | SOS,D,number 1,number 2,number 3# | SOS,D,1# SOS,D,1,2# SOS,D,1,2,3# Option to delete 1 or more numbers at a time |
| 21 | Query SOS number | SOS# | Reply： SOS:8613912345678,8613912345678,8613912345678 |
| 22 | Allow auto answering | 777# | Reply:Automatic incoming call answering has been set After setting, the device will answer the call automatically after any number |
| 23 | Disable automatic answering | 888# | Reply:Automatic incoming call answering has been Close After setting, the device will answer the call automatically after SOS or center number (default: forbidden) |
| 24 | Set the incoming call function | SZCS#CALL_FUN=A | A=0 voice monitoring function after incoming calls（default,it needs device support microphone） A=1 reply to google link after incoming call SMS：SZCS#CALL_FUN=1 Reply：SETOK: CALL_FUN=1 |
| 25 | Query the incoming call function | CXCS#CALL_FUN | Reply：READOK: CALL_FUN=1 |
| 26 | Heartbeat packet setting interval | HBT,T1,T2# T1=60-300seconds，ACC ON heartbeat packet upload interval T2=60～300 minutes，ACC OFF heartbeat packet upload interval | SMS:HBT,180,180# Reply：HBT ACC ON:180s,ACC OFF:180s |
| 27 | Query heartbeat packet interval time | HBT# | Reply:HBT ACC ON:180s,ACC OFF:180s |
| 28 | Set GPS data timing sending interval | TIMER,T1,T2# T1=5～60 seconds；Upload interval in ACC ON state T2=5～1800seconds；Upload interval in ACC OFF state | SMS ：TIMER,30,300# Reply ：TIMER ACC ON:30s,ACC OFF:300s |
| 29 | Query GPS data timing sending interval time | TIMER# | Reply :TIMER ACC ON:30s,ACC OFF:300s |
| 30 | Turn on vibration alarm settings | SENALM,A,M# A=ON M=0～2；Alarm reporting method，0 only GPRS，1 SMS+GPRS，2 GPRS+SMS+CALL； | SMS ：SENALM,ON,2# Reply ：SENALM:ON,2 |
| 31 | Turn off vibration alarm settings | SENALM,OFF# | Reply ：SENALM:OFF |
| 32 | Query vibration alarm setting parameters | SENALM# | Reply ：SENALM:OFF |
| 33 | Enable power-off alarm settings | POWERALM,A,M,T1,T2,# A=ON M=0～2；0 only GPRS，1 SMS+GPRS，2 GPRS+SMS+CALL T1=2～60seconds；Power off detection time T2=1-3600seconds minimum charging time | SMS：POWERALM,ON,2,10,10,# Reply ：POWERALM:ON,2,10,10 |
| 34 | Turn off the power-off alarm | POWERALM,OFF# | Reply ：POWERALM:OFF |
| 35 | Query power-off alarm status | POWERALM# | Reply ：POWERALM:ON,2,10,10 |
| 36 | Enable low battery alarm settings | BATALM,A,M# A=ON M=0～1 0 represents： only GPRS，1 represents：SMS+GPRS， | SMS ：BATALM,ON,1# Reply ：BATALM:ON,1 |
| 37 | Turn off low battery alarm settings | BATALM,OFF# | Reply ：BATALM:OFF |
| 38 | Query the low battery alarm status | BATALM# | Reply ：BATALM:ON,1 |
| 39 | Enable movement alarm settings | MOVING,A,R,M# A=ON R=100～1000；movement radius M=0～2；0 only GPRS，1 SMS+GPRS；2 GPRS+SMS+CALL | SMS：MOVING,ON,1000,2# Reply ：MOVING:ON,1000,2 |
| 40 | Turn off movement alarm | MOVING,OFF# | Reply ：MOVING:OFF |
| 41 | Query the movement setting status | MOVING# | Reply ：MOVING:ON,1000,2 |
| 42 | Turn on overspeed alarm | SPEED,A,B,C,M# A=ON B=5～600 seconds；over speed time C=1～255km/h；speed setting M=0～1；Alarm reporting method，0 only GPRS，1SMS+GPRS； | SMS：SPEED,ON,10,120,1# Reply ：SPEED:ON,10,120,1 |
| 43 | Turn off over speed alarm | SPEED,OFF# | Reply ：SPEED:OFF |
| 44 | Query overspeed setting status | SPEED# | Reply ：SPEED:ON,10,120,1 |
| 45 | Turn on ACC ignition on alarm | ACCALM,A,M# A=ON M=0～3 0 ：only GPRS， 1 ：GPRS+SMS， 2 ：GPRS+CALL, 3 ：GPRS+SMS+CALL | SMS ：ACCALM,ON,3# Reply ：ACCALM:3,OK |
| 46 | Turn off ACC ignition on alarm | ACCALM,OFF# | Reply ：ACCALM,OFF OK |
| 47 | Query ACC ignition on alarm | ACCALM# | Reply ：ACCALM:3,OK |
| 48 | Turn on the ACC off alarm | ACCOFFALM,A,M# A=ON M=0～3 0 ：only GPRS， 1 ：GPRS+SMS， 2 ：GPRS+CALL, 3 ：GPRS+SMS+CALL | SMS：ACCOFFALM,ON,3# Reply ：ACCOFFALM:3,OK |
| 49 | Turn off the ACC off alarm | ACCOFFALM,OFF# | Reply ：ACCOFFALM,OFF OK |
| 50 | Query ACC off alarm | ACCOFFALM# | Reply ：ACCOFFALM:3,OK |
| 51 | Query the sleep working mode | CXCS#SLPDISCONNECT | Reply ：READOK: SLPDISCONNECT=0 |
| 52 | SMS time zone settings | GMT,A,B,C# | A: E or W;"E" means eastern time zone, "W" means western time zone;default: E B: 0～12;time zone default: 8 C: 0/15/30/45;half time zone;default: 0 SMS：GMT,E,8,0# Reply ：GMT:E,8,0 |
| 53 | SMS time zone query | GMT# | Reply ：GMT:E,8,0 |